# Introduction
The AlarmPi software is written in Java and consists of 2 parts:
- the actual alarm clock running on a Raspberry Pi as a headless deamon that gets started automatically when the Pi boots up
- the remote control GUI which is an Android App
The daemon uses the following open source libraries:
- ini4j (http://ini4j.sourceforge.net)
  Used to read configuration files in .ini format. Licensed under the Apache License, Version 2.0 (http://www.apache.org/licenses/LICENSE-2.0)
- Pi4J (http://pi4j.com)
  Used to interface with Raspberry Pi GPIOs from Java. Pi4J itself depends on WiringPi (http://wiringpi.com) licensed under GNU LGPLv3 license (http://www.gnu.org/copyleft/lesser.html)
# The PCB
The AlarmPi PCB holds some very simple circuits and basically serves as mechanical fixture for the various components like LED constant current source(s) or the PCA9685 module.
Schematics:

PCB:

# Parts List (BOM)
Amount	Description	Supplier
1	Raspberry Pi 2/3
1	HiFiBerry DAC+ standard - Phone jack version	hifiberry.com
4	2mm Nylon spacer + screw (M2.5)	hifiberry.com
1	PCA9685 16-Channel 12-bit PWM I2C Module	Ebay
1	Stiftleiste (Standard) Anzahl Reihen 2 Polzahl je Reihe 20	Conrad 737575 - 62
2	Stiftleiste (Standard) Anzahl Reihen: 1 Polzahl je Reihe: 8	Conrad 742235 - 62
1	Buchsenleiste (Präzision) Anzahl Reihen 2 Polzahl 40	Conrad 738472 - 62
1	Schraubklemmblock 1.50 mm² Polzahl 2	Conrad 731986 - 62
2	Schraubklemmblock 0.75 mm² Polzahl 4	Conrad 567658 - 62
1	Schraubklemmblock 0.75 mm² Polzahl 3	Conrad
1	Schraubklemmblock 0.75 mm² Polzahl 2	Conrad

1	DCDC converter TracoPower TSR 1-2450 24 V/DC 5 V	Conrad 156673 - 62
1	PhotoMOS-Relais AQY_EH-Serie Panasonic AQY212GH	Conrad 504873 - 62
1	USB Type A Buchse, horizontal	Conrad 1088207 - 62
1	Resistor 1K0Ohm (PCA9685 OE/ 3.3V pull-up)
1	Resistor 470Ohm (PhotoMos LED forward current)
1	Electrolytic Capacitor 47uF (PWM module decoupling)
2	C 220nF (input keys debouncing)

# Raspberry GPIOs
The following Raspberry Pi pins from header P1 are used by AlarmPi:
pin#	RPI name	WiringPi	Used For
3	gpio2, I2C SDA	gpio8	HiHiBerry and PCA9685 I2C control
5	gpio3, I2C SCL	gpio9	HiHiBerry and PCA9685 I2C control
12	gpio18	gpio1	HiFiBerry sound interface
35	gpio19	goio24	HiFiBerry sound interface
38	gpio20	gpio28	HiFiBerry sound interface
40	gpio21	gpio29	HiFiBerry sound interface
16	gpio23	gpio4	USB Audio Power on/off
22	gpio25	gpio6	Input key 1
18	gpio24	gpio5	Input key 2
36	gpio16	gpio27	LED PWM OE
19	gpio10	gpio12	SPI MOSI (typically not used)
23	gpio11	gpio14	SPI SCLK (typically not used)

# Installation
The following instructions are based on the Raspbian Jessie Lite image Version May 2016 (Kernel version 4.4) and assume that the network setup is working in your environment
- run raspi-config
  sudo raspi-config
  and make sure the following settings are done:
  - 1 Expand Filesystem
  - 3 Boot Options -> B1 Console
  - 5 Internationalisation Options -> I2 Change Timezone to you locale timezone
  - 9 Advanced Options -> A4 SSH enabled
  - 9 Advanced Options -> A5 SPI enabled
  - 9 Advanced Options -> A6 I2C enabled
- Make sure all packages are up to date
  sudo apt-get update
  sudo apt-get upgrade
- Update the Raspberry firmware
  sudo apt-get install rpi-update
  sudo rpi-update
- reboot
  sudo reboot
- Install the Music Player Daemon (mpd)
  sudo apt-get install mpd mpc alsa-utils
- Install Java8 runtime environment
  sudo apt-get install openjdk-8-jre
- x
- x
- Create directories required by AlarmPi:
  sudo mkdir /opt/alarmpi
  sudo mkdir /var/log/alarmpi
  sudo mkdir /etc/opt/alarmpi
  sudo mkdir /var/lib/mpd/music/tmp
  sudo chown -R mpd:audio /var/lib/mpd/music
- copy the alarmpi files to their target folders:
  sudo cp alarmpi /etc/init.d
  sudo cp alarmpi.jar /opt/alarmpi
  sudo cp alarmpi.cfg /etc/opt/alarmpi
  sudo cp alarmpi.logging /etc/opt/alarmpi
  sudo cp alarm*.mp3 /var/lib/mpd/music
- adopt the settings in /etc/opt/alarmpi/alarmpi.cfg and try to start AlarmPi by
  sudo chmod +x /etc/init.d/alarmpi
  sudo /etc/init.d/alarmpi start
- check the logfiles in /var/log/alarmpi for errors and fix them if needed. Use
  sudo /etc/init.d/alarmpi restart
  to restart alarmpi after a change in the configuration file
- check the communication to the AlarmPi TCP server
  nc 127.0.0.1 3947
  connected to AlarmPi
  command:
  help
  should return a list of commands supported by alarmpi
- Create a set of alarms
  Creation of alarms is not supported by the App and must be done manually. Create any number of alarms with
  alarm add – 00:00 0
  terminate the connection to AlarmPi with
  exit
- Configure init.d to start AlarmPi automatically at system boot with
  sudo update-rc.d alarmpi defaults
- tbd
# Start using it