# Pi OS & HiFiBerry Configuration
Based on Raspberry Pi 3 and Raspberry Pi OS (64bit) Bookworm, release date 2024-11-19
- configure Pi OS
  sudo rpi-config
- update all packages
  sudo apt-get update
  sudo apt-get upgrade
- Configure the kernel for HiFiBerry DAC+
  sudo nano /boot/firmware/config.txt
- comment out the line
  dtparam=audio=on
- update this line
  dtoverlay=vc4-kms-v3d,noaudio
- add the line
  dtoverlay=hifiberry-dacplus
- create the file /etc/asound.conf with the following content:
  pcm.!default {
   type hw card 0
  }
  ctl.!default {
   type hw card 0
  }
- verify the setup with
  aplay -l
- expected output
  **** List of PLAYBACK Hardware Devices ****
  card 0: sndrpihifiberry [snd_rpi_hifiberry_dacplus], device 0: HiFiBerry DAC+ HiFi pcm512x-hifi-0 [HiFiBerry DAC+ HiFi pcm512x-hifi-0]
   Subdevices: 1/1
   Subdevice #0: subdevice #0
# Installation of AlarmPi daemon pacckage
- Create installation package
  createInstallationPackage
- copy alarmpi.tar.gz onto the Raspberry Pi and untar it into a temp folder
- change to the scripts folder
- run
  ./install

- change password of user alarmpi and grant sudo permissions
  sudo passwd alarmpi
  sudo usermod -aG sudo alarmpi
- adopt configuration in /etc/alarmpi/alarmpi.cfg and /etc/alarmpi/alarmpi.logging
# Install NTP
- sudo apt-get install ntp
- sudo systemctl status ntp
# Further configuration steps
- Configure mpd by editing /etc/mpd.conf and set this audio_output configuration:
  audio_output {
  type "alsa"
  name "HiFiBerry"
  device "hw:0,0"
  mixer_type "software"
  # mixer_device "default" # optional
  # mixer_control "PCM" # optional
  # mixer_index "0" # optional
  }
- make sure mpd log directory exists
  as we will move /var/log to a tmpfs filesystem, we have to make sure the mpd log directory exists before mpd gets started. Add the following line to the file /lib/systemd/system/mpd.service in the [Service] section (before ExecStart):
  ExecStartPre=-/bin/mkdir /var/log/mpd
- enable mpd service
  sudo systemctl enable mpd
- edit /etc/lighttpd/lighttpd.conf and change this line:
  server.document-root = "/opt/alarmpi/www"
- make sure lighttpd log directory exists
  as we will move /var/log to a tmpfs filesystem, we have to make sure the lighttpd log directory exists before lighttpd gets started. Add the following line to the file /lib/systemd/system/lighttpd.service in the [Service] section (as first line):
  ExecStartPre=-/bin/mkdir /var/log/lighttpd
  ExecStartPre=-/bin/chown www-data:www-data /var/log/lighttpd
# Configuration of the watchdog
- enable the watchdog
  sudo modprobe bcm2835_wdt
- install the watchdog daemon
  sudo apt-get install watchdog
- configure the watchdog
  sudo nano /etc/watchdog.conf
- uncomment the lines
  max-load-1 = 24
  watchdog-device = /dev/watchdog
  and add these lines
  file = /var/log/alarmpi/watchdog
  change = 300
- adopt the settings in /lib/systemd/system/watchdog.service
  sudo nano /lib/systemd/system/watchdog.service
  and add this line at the end of the [Install] section:
  WantedBy=alarmpi.service
  and add this line to the start of the [Service] section:
  ExecStartPre=-sudo -u alarmpi /usr/bin/touch /var/log/alarmpi/watchdog
- adopt the settings in usr/lib/systemd/system/alarmpi.service
  sudo nano /usr/lib/systemd/system/alarmpi.service
  and add this line at the end of the [unit]section:
  Before=watchdog.service
- execute
  sudo systemctl enable watchdog.service
  sudo systemctl daemon-reload
  sudo systemctl start alarmpi.service

# Reduce risk of filesystem corruption
The internet is full of reports that the SD card can easily get corrupted during a power outage und otherwise unclean shutdown, and in fact it also happened to one of my Raspberries once. The best way to avoid this is to change to a completely read-only filesystem. I did not go that far but took some actions to at least minimize the risk of corruption (based on many guides you will find on the web)
- Direct system logging into a circular memory buffer with
  sudo apt-get install busybox-syslogd
  sudo apt-get purge rsyslog
  log messages can now be read using logread.
- Create RAM (tmpfs) filesystems for directories that are frequently written, but the content does not need to survive reboots of the system.
  Add the following lines to /etc/fstab:
  tmpfs /var/log tmpfs defaults,noatime,nosuid,mode=0755,size=10m 0 0
  tmpfs /tmp tmpfs defaults,noatime,nosuid,mode=0755,size=10m 0 0
  tmpfs /var/lib/mpd/music/tmp tmpfs	defaults,noatime,nosuid,mode=0755,size=10m 0 0
- disable swapping by adding noswap to the end of /boot/firmware/cmdline.txt
# Disable WLAN and Bluetooth
sudo nano /boot/config.txt
 # turn wifi and bluetooth off
dtoverlay=pi3-disable-wifi
dtoverlay=pi3-disable-bt
and disable hciuart
sudo systemctl disable hciuart
sudo reboot

edit /etc/rc.local and add
/usr/sbin/rfkill block bluetooth # Disable Bluetooth
/usr/sbin/rfkill block wifi # Disable WiFi
# Voice control using Amazon Web Services Lex

## Installation of the USB microphone
- Tested with a Foxnovo Portable USB 2.0-Kondensator-Mikrophone
- Connect to one of the raspberry USB ports
- lsusb
  should show an output like
  Bus 001 Device 004: ID 0d8c:013c C-Media Electronics, Inc. CM108 Audio Controller
- alsamixer
  press F6 and select the USB soundcard (in my case: USB PnP Sound Device) and remember the ID
- exit alsamixer with Escape
- record a 5s test with
  arecord -f S16_LE -r 16000 -d 5 -vv -D plughw:<id> test.wav
- XXX

- Create an AWS account (free for 12 months) on https://aws.amazon.com/
- Create an Administrator IAM User on https://console.aws.amazon.com/iam
- Create an user alarmpi with only programmatic access to LEX services
- create a file /etc/alarmpi/.aws/credentials with this content:
  [default]
  aws_access_key_id=<your access key id>
  aws_secret_access_key=<your secrest access key>

# Powersaving and LEDs off
https://forums.raspberrypi.com/viewtopic.php?t=257144
switch HDMI off:
edit /etc/rc.local and add
tvservice -o
switch off LEDs

edit bootconfig.txt and add
##turn off mainboard LEDs
dtoverlay=act-led

##disable ACT LED
dtparam=act_led_trigger=none
dtparam=act_led_activelow=off

##disable PWR LED
dtparam=pwr_led_trigger=none
dtparam=pwr_led_activelow=off

##turn off ethernet port LEDs
dtparam=eth_led0=4
dtparam=eth_led1=4
##turn on/ off bluetooth
dtoverlay=disable-bt

##turn on/off wifi
dtoverlay=disable-wifi

# Enable DRM VC4 V3D driver on top of the dispmanx display stack
dtoverlay=vc4-fkms-v3d
max_framebuffers=2